## Slide 1: EJ-FAT
Stacey Sheldon
Yatish Kumar, Michael Goodrich, Graham Heyes
Notes: ‹#›

## Slide 2: End to End science problem and motivation
*
SC22 | Dallas, TX | hpc accelerates.
‹#›
Compute Node
ESNET
DOE needs to stream N x 400G A/D samples from very large instruments to its HPC / Supercomputers for processing
Extreme Scale Streaming ( 400G / 800G / 1.2T … )
Very long latencies across North America ( 30 ms / 60 ms … )
No time for retransmission. Data loss is treated as “noise” and compute keeps going
Compute Node
Compute Node
Compute Node
Compute Node
Compute Node
Compute Node
Compute Node
DAQ
DAQ
DAQ
DAQ

## Slide 3: End to End science problem and motivation
*
SC22 | Dallas, TX | hpc accelerates.
‹#›
DOE has dozens of large instruments spread out across the country
Each instrument will produce Nx400G streams of DAQ data based on emerging sensors
This requires real time processing in order to:
  Preview and tune the experiment to ensure well focused beams, x-rays and samples
  Use compute to identify events, particles, image frames etc.
    Select what to store
    Discard the raw DAQs for up to 1000000:1 data reduction
Compute Node
ESNET
Compute Node
Compute Node
Compute Node
Compute Node
Compute Node
Compute Node
Compute Node
DAQ
DAQ
DAQ
DAQ

## Slide 4: Design Goals
DAQ
DAQ
DAQ
DAQ
EJ-FAT
FPGA + Switch
Compute Node
Compute Node
ESNET
Unidirectional UDP Stream
1) Separation of IP Addresses
2) In network sorting of Event Data
3) Stateless load balancing
4) Compute node feedback for dynamic LB
5) Hit-less reconfiguration of LB table
6) Unidirectional UDP streaming
AS: 345 203.58.0.0/16
AS: 999 102.12.2.0/8
Event Q Feedback

## Slide 5: Implementation - Data Plane Packet Rewrite
Eth
LB IP
UDP
LB
Data
Eth | LB Dst MAC | Next HOP Router / CN MAC
IP | LB Dst IP | CN Dst IP
UDP | LB well known port | CN UDP Dst port
LB | Event ID | — Header Popped
Eth
CN IP
UDP
Data
** Fine Print : Src IP rewritten to LB IP, ARP/ND used to resolve next-hop Dst MAC, UDP Dst port used to select a CPU within the CN, LB responds to upstream ARP/ND/ping, packets dropped if wrong Eth, IP addr/port or LB header.

## Slide 6: Implementation - Data Plane Selecting a CN
Event ID
Event ID
0
8
63
> 53,000 | last epoch
> 209,000 | this epoch
TBD | next epoch
unused | —-
0 | CN #A
1 | CN #B
… | CN #B
511 | CN #Z
CN A | ETH | IP | UDP
CN B | ETH | IP | UDP
CN Y | ETH | IP | UDP
etc.. |  |  | 
9
Select Epoch
Select
Calendar
Slot
0 | CN #Y
1 | CN #Y
… | …
511 | CN #Z
0 | CN #Y
1 | CN #O
… | …
511 | CN #W
Compute Node Details
Multiple active epoch tables ensures make before break forwarding
Atomic transition between epochs on event # boundaries
Multiple entries for the same CN controls “weight” of that CN
512 entry epoch table balances table size vs. # CN
  it is adjustable by recompiling the FPGA
Indirection for CN Details, helps compress memory and speeds up table programming

## Slide 7: Implementation - Control Plane Updating the LB
Time
0 | CN 0
1 | CN 1
2 | CN 2
N | CN 1
Start with a default LB
CN 0 | oooo______
CN 1 | oooooooo__
CN 2 | o_________
Monitor CN Q Fill
Build a new epoch table
Activate New Epoch
Release Old Epoch
Wait
0 | CN 0
1 | CN 1
2 | CN 2
N | CN 1
0 | CN 0
1 | CN 1
2 | CN 2
N | CN 1
CN 0 | oooo______
CN 1 | ooooo_____
CN 2 | oooo______
Monitor CN Q Fill
0 | CN 0
1 | CN 1
2 | CN 2
N | CN 2
0 | CN 0
1 | CN 1
2 | CN 2
N | CN 2
0 | CN 0
1 | CN 1
2 | CN 2
N | CN 2

## Slide 8: Test Setup
DAQ Source Emulator
Real Load Balancer HW
Compute Node
DAQ Packet Sequence Generator SW
DAQ.pcapng
DPDK pcap Replay
- multi DAQ
- network jitter
- random order DAQ
- event overlap
FPGA Server
Compute Node Server
U280 FPGA
PCIe @ 100Gpbs Packet Inject + P4 Table Config
tcpdump
- HW TS (ns)
- 100Gbps Rx
CN.pcapng
Ethernet @ 100Gpbs
This is the physical setup for the test results in this paper: - It is a packet level test centered on the LB
Streaming has been done in a larger system, with full science streaming and reconstruction

## Slide 9: Test Results

## Slide 10: Thank You
Contact : smartnic@es.net
Implemented using : https://github.com/esnet/esnet-smartnic-hw